## Slide 1: (WoT IG‘s architecture document) Overview Architecture of WoT Servient
WoT Servient
Client Connector
Server Connector
Protocol Binding
Resource Model
App Script
Legacy comm-unication
Server API
Client API
Thing
Description
Legacy
device
Web Client
Web Server
Proprietary interface
Runtime Environment
WoT Servient
WoT Servient
App Script:
Implements application logic in a modular and portable way. It can access local hardware, locally connected legacy devices, and remote things through the WoT Interface. For this, the runtime environment must provide the Scripting API (Physical, Client, Server).
Resource Model:
Provides a common abstraction across the different protocols. Just like the Web, it allows to identify and address interaction points with URIs.
Protocol Binding:
Converts interactions with devices using information in TD in accordance with lower layer protocols. For legacy devices, adapters available for those devices convert the protocol.
Thing Description:
Declares providing API name, parameter type and so on. External client refers this description to call WoT Interface.
WoT Interface
Discovery API
(Propr. API)

## Slide 2: Overview Architecture of WoT Servient
WoT Servient
Protocol Binding
App Script
Legacy comm-unication
Server
API
Client
API
Thing
Description
Legacy
device
Web Client
Web Server
Proprietary Protocol
Runtime Environment
WoT Servient
WoT Servient
Discovery
API
Scripting API
Binding Template
Security
and
Privacy
Local
Hardware
WebSocket
MQTT
HTTP
CoAP
Proprietary API
Security Option
Thing Description:
Metadata and declarations of thing’s capabilities
(e.g., possible interactions).
Providing the definition of different machine-
understandable vocabulary sets as well as
serialization formats.

## Slide 3: Overview Architecture of WoT Servient
WoT Servient
Protocol Binding
App Script
Legacy comm-unication
Server
API
Client
API
Thing
Description
Legacy
device
Web Client
Web Server
Proprietary Protocol
Runtime Environment
WoT Servient
WoT Servient
Discovery
API
Scripting API
Binding Template
Security
and
Privacy
Local
Hardware
WebSocket
MQTT
HTTP
CoAP
Proprietary API
Security Option
Scripting API:
APIs for interactions with Things and reactions/handlers to provide the functionality
of a Thing.
Scripting APISs can be classified into 4 categories
as follows;
1) Client API which supports consuming Things
2) Server API which supports exposing Thingss
3) Discovery API which supports abstract method
to access discovery mechanism
4) Security option which includes authentication,
authorization and secure communications
Security API is not independent from other
APIs and it is included in other APIs with
parameters and so on

## Slide 4: Overview Architecture of WoT Servient
WoT Servient
Protocol Binding
App Script
Legacy comm-unication
Server
API
Client
API
Thing
Description
Legacy
device
Web Client
Web Server
Proprietary Protocol
Runtime Environment
WoT Servient
WoT Servient
Discovery
API
Scripting API
Binding Template
Security
and
Privacy
Local
Hardware
WebSocket
MQTT
HTTP
CoAP
Proprietary API
Security Option
Binding Templates:
Standard binding templates for most common protocols which used in Protocol Binding block.
Supported transfer communication patterns are push, pull, pub-sub and bi-directional messaging. e.g., REST-based protocols such as HTTP and CoAP, pub-sub protocols such as MQTT, and raw channel-based protocols such as WebSockets.

## Slide 5: Overview Architecture of WoT Servient
WoT Servient
Protocol Binding
App Script
Legacy comm-unication
Server
API
Client
API
Thing
Description
Legacy
device
Web Client
Web Server
Proprietary Protocol
Runtime Environment
WoT Servient
WoT Servient
Discovery
API
Scripting API
Binding Template
Security
and
Privacy
Local
Hardware
WebSocket
MQTT
HTTP
CoAP
Proprietary API
Security Option
Security and Privacy:
Cross-cutting mechanism for security and privacy over Thing Description, Scripting API and Protocol Bindings
Thing Description and Scripting API will support both transport and object security using best practices.
Binding Templates will support the use of appropriate for the protocols they map to.
It includes requirements of network and web-based technologies for implementation.

## Slide 6: Overview Architecture of WoT Servient
WoT Servient
Protocol Binding
App Script
Legacy comm-unication
Server
API
Client
API
Thing
Description
Legacy
device
Web Client
Web Server
Proprietary Protocol
Runtime Environment
WoT Servient
WoT Servient
Discovery
API
Scripting API
Binding Template
Security
and
Privacy
Local
Hardware
WebSocket
MQTT
HTTP
CoAP
Proprietary API
Security Option
Local Hardware:
When Thing is included inside of WoT Servient as local hardware, then implemented runtime environment accesses the thing through proprietary APIs such as W3C Device API, and so on.
This block is out of scope of WoT standardization, but sometimes touched on as implementation practices and/or liaison with other W3C WG and SDOs.

## Slide 7: Overview Architecture of WoT Servient
WoT Servient
Protocol Binding
App Script
Legacy comm-unication
Server
API
Client
API
Thing
Description
Legacy
device
Web Client
Web Server
Proprietary Protocol
Runtime Environment
WoT Servient
WoT Servient
Discovery
API
Scripting API
Binding Template
Security
and
Privacy
Local
Hardware
WebSocket
MQTT
HTTP
CoAP
Proprietary API
Security Option
Legacy Communication
When Thing is outside of WoT Servient and is connected to WoT servient with legacy IoT protocols, then implemented runtime environment utilizes Legacy Communication such as Echonet Lite and so on through proprietary APIs.
Especially, constraint devices such as simple sensors with low speed CPU can be accessed through simple protocols by gateway which has higher spec resources. Then WoT servient for the sensors can be implemented in gateway on behalf of each sensor hardware utilizing Legacy Communication block.
This block is out of scope of WoT standardization, but sometimes touched on as implementation practices and/or liaison with other W3C WG and SDOs.

## Slide 8: Overview Architecture of WoT Servient
WoT Servient
Protocol Binding
App Script
Legacy comm-unication
Server
API
Client
API
Thing
Description
Legacy
device
Web Client
Web Server
Proprietary Protocol
Runtime Environment
WoT Servient
WoT Servient
Discovery
API
Scripting API
Binding Template
Security
and
Privacy
Local
Hardware
WebSocket
MQTT
HTTP
CoAP
Proprietary API
Security Option
App Script
As client and/or Server, logic is implemented in App Script which utilizing WoT Scripting API and proprietary API mainly used to access Thing.